## Slide 1: Ohm’s Law in 5 Minutes
V = IR
Voltage = Current*Resistance

## Slide 2: A circuit is like a slide (sort of)
Analogy and graphics credit to Dean Baird’s “Book of Phyz”:
http://phyz.org/phyz/BOP/10-CIRCUITS/G-Circuit_Slider.pdf

## Slide 3: The riders are like units of Charge (Q) The height is like Voltage (V)
V
V
Charge (Q), measured in Coulombs (C), an SI base unit, essentially the number of electrons
Voltage (V), measured in Volts (V), units J/C, the amount of work each unit charge is capable of
Analogy and graphics credit to Dean Baird’s “Book of Phyz”:
http://phyz.org/phyz/BOP/10-CIRCUITS/G-Circuit_Slider.pdf

## Slide 4: Current (I) is the rate of rider flow, A “short circuit” is like a ladder with no slide
Analogy and graphics credit to Dean Baird’s “Book of Phyz”:
http://phyz.org/phyz/BOP/10-CIRCUITS/G-Circuit_Slider.pdf
Current (I), measured in Amperes (A), units C/s, the rate of flow of charge

## Slide 5: And finally, Resistance (R) is like the run length
Analogy and graphics credit to Dean Baird’s “Book of Phyz”:
http://phyz.org/phyz/BOP/10-CIRCUITS/G-Circuit_Slider.pdf
Resistance (R), measured in Ohms (Ω), units A/V, a measure of the obstruction to flow of charge of a body

## Slide 6: A voltage V, applied to resistor R, will cause charge to flow from higher V to lower V with current I
I
“Ground” symbol, a shorthand for 0 Volts
V = IR
I = V/R
R = V/I
We can calculate V, I or R,
if we have the other 2

## Slide 7: The voltage divider
From Ohm’s law, it can be shown that:
Ask about my derivation!!!
If R2 = R1,
V2 = V1/2

## Slide 8: A “Thermistor” is a Resistor whose Resistance varies with Temperature
Vcc is shorthand for a fixed power supply voltage
RT is now a thermistor
Vsig now varies with temperature,
Creating a SIGNAL
If we measure Vsig, we now have a temperature sensor!